## Slide 1
Cosmos Policy
Inference Pipeline
Direct Policy Inference Flow | RoboCasa Platform
NVIDIA Cosmos Policy — Video Foundation Model for Robot Control
Each slide covers one module: Input -> Function -> Output -> Code Location
Observation
→
Tokenize
→
Condition
→
Noise
→
DiT
→
Denoise
→
Decode
→
Action
Cosmos Policy Inference Pipeline — RoboCasa
1 / 20

## Slide 2
流水线总览
Pipeline Overview
Cosmos Policy Inference Pipeline — RoboCasa
2 / 20
1. Observation
Collect
→
2. VAE
Encode
→
3. Latent
Layout
→
4. Condition
Mask
→
5. Text
Condition
→
6. Noise
Schedule
→
7. DiT
Denoise
→
8. EDM
Precond
→
9. Iterative
Sample
10. VAE
Decode
→
11. Action
Extract
→
12. Proprio
Extract
→
13. Robot
Execute
→
14. Open-Loop
Control
→
15. Best-of-N
Planning
→
16. Value
Predict
→
17. Multi-View
Fusion
→
18. Training
vs Inference
NOTE
RoboCasa Config: state_t=11 observation frames, chunk_size=32 action steps, action_dim=7, proprio_dim=9
3 camera views (agentview, eye_in_hand, robot0_robotface). Total latent frames = 11 video + 8 action + 2 proprio = 21 frames
Each latent frame shape: (1, 16, 28, 28) for 224x224 input with 8x spatial compression
CODE: cosmos_policy/constants.py | cosmos_policy/experiments/robot/cosmos_utils.py:61-85 | cosmos_policy/config/experiment/cosmos_policy_experiment_configs.py

## Slide 3
模块 1: 观测数据收集
Observation Data Collection
Cosmos Policy Inference Pipeline — RoboCasa
3 / 20
⬅ INPUT
Raw sensor data from RoboCasa simulation environment:
- 3x camera images: (B, 3, 224, 224) each [agentview, eye_in_hand, robotface]
- Proprioceptive state: (B, 9) [joint pos(7) + gripper(2)]
- Task language instruction: string, e.g. 'pick up the red block'
⚙ FUNCTION
Collect multi-modal observations from the robot environment.
1. Capture RGB images from 3 calibrated cameras at 224x224 resolution.
2. Read robot joint positions (7-DOF) + gripper state (2 values) = 9-dim proprio.
3. Receive natural language task description.
4. Stack history: state_t=11 frames of observation history.
5. Images normalized to [-1, 1] range, proprio normalized per-dimension.
➡ OUTPUT
Processed observation tensors:
- images_list: List[Tensor] of length 3, each (B, 3, 224, 224)
- proprio: (B, 9) normalized joint + gripper state
- task_text: str, language instruction for the episode
DATA FORMAT
RoboCasa dataset: HDF5 format with observations/qpos/gripper_state/actions fields
state_t=11 means 11 frames of history are stacked as context
CODE: cosmos_policy/experiments/robot/cosmos_utils.py:851 get_action() | cosmos_policy/experiments/robot/cosmos_utils.py: prepare_data_batch()

## Slide 4
模块 2: VAE 编码器 (视频分词)
WAN 2.1 VAE Encoder — Video Tokenization
Cosmos Policy Inference Pipeline — RoboCasa
4 / 20
⬅ INPUT
Raw video frames: (B, 3, T, H, W)
- For each camera view: (B, 3, state_t=11, 224, 224)
- Pixel range: [-1, 1] (normalized)
- 3 independent camera streams encoded separately
⚙ FUNCTION
WAN 2.1 Video VAE Encoder compresses pixel-space video to compact latent space.
1. Spatial: 8x downsample via 2D convolutions (224->112->56->28).
2. Temporal: 4x downsample via 3D causal convolutions (groups of 4 frames).
3. Channel: 3 (RGB) -> 16 (latent channels).
4. KL regularization keeps latents in a well-behaved distribution for diffusion.
5. Each camera view is independently encoded.
6. state_t=11 frames -> ceil(11/4)=3 temporal latent frames per view.
➡ OUTPUT
Latent representations: (B, z_dim=16, T', H', W')
- Per camera: (B, 16, 3, 28, 28) [T'=11/4=2.75 -> padded to 3 temporal frames]
- Spatial compression: 224/8 = 28
- Temporal compression: 4x (4 pixel frames -> 1 latent frame)
- Latent space: continuous, learned by KL-regularized VAE
COMPRESSION
Total compression ratio: 8x spatial * 4x temporal = 32x
Each 224x224 RGB frame -> 1x28x28x16 latent = 12,544 values (vs 150,528 pixels)
CODE: cosmos_policy/tokenizers/wan2pt1.py:197 class CosmosPolicyWanVAE | :303 encode() | :44 class WanVAE_ | :51 encode()

## Slide 5
模块 3: 隐帧布局 (隐变量帧注入)
Latent Frame Injection & Sequence Layout
Cosmos Policy Inference Pipeline — RoboCasa
5 / 20
⬅ INPUT
Observation latents + Action/Proprio/Value metadata:
- 3x camera latents: each (B, 16, 3, 28, 28)
- Action chunk: (B, 32, 7) = 224 values, all zeros at inference
- Proprio state: (B, 9) values
- Value placeholder: scalar (for planning mode)
⚙ FUNCTION
Key Innovation: Encode all modalities into a UNIFIED latent frame sequence.
1. Action Latent Injection: 224 action values (32x7) repeat-filled into 8 latent frames.
Each frame has 16*28*28=12,544 slots, first 224/8=28 values set per frame (repeat padding).
2. Proprio Injection: 9 values repeat-filled into 2 latent frames similarly.
3. Temporal duplication: WAN VAE maps 4 pixel frames -> 1 latent frame, so each
concept needs 4 identical images to produce 1 latent frame (handled in training).
4. At inference: action/proprio frames initialized as NOISE (to be denoised).
➡ OUTPUT
Full latent sequence: (B, 16, total_frames, 28, 28)
RoboCasa layout (21 frames total):
Frame 0-2: camera1 latents (3 frames)
Frame 3-4: camera2 latents (2 frames)
Frame 5-6: camera3 latents (2 frames)
Frame 7-14: action latents (8 frames, 32 steps * 7 dims mapped)
Frame 15-16: proprio latents (2 frames, 9 dims mapped)
Frame 17-20: future state prediction (4 frames)
PRINCIPLE
Treats robot actions as 'fake video frames' - same diffusion process denoises video AND predicts actions.
This is the core insight: unified multimodal generation via shared latent space.
CODE: cosmos_policy/models/policy_text2world_model.py:45 replace_latent_with_action_chunk() | :112 replace_latent_with_proprio()

## Slide 6
模块 4: 条件掩码
Condition Mask — Clean vs. Denoise Frames
Cosmos Policy Inference Pipeline — RoboCasa
6 / 20
⬅ INPUT
Full latent sequence: (B, 16, 21, 28, 28)
- Video observation frames: known/clean (encoded from real observations)
- Action/proprio/future frames: unknown at inference (need denoising)
⚙ FUNCTION
Binary mask that tells the model which frames are 'given' vs 'to predict'.
1. Observation frames (mask=1): These are CLEAN latents from VAE encoder.
During diffusion, noise is NOT added to these frames.
2. Action/Proprio/Future frames (mask=0): These are TARGETS for denoising.
During training, noise IS added; model learns to denoise them.
3. At inference: observation frames stay fixed, action frames start from pure noise
and are iteratively denoised to produce action predictions.
4. Enables flexible conditioning: different frame types can be clean or noisy.
➡ OUTPUT
Binary condition mask: (B, 1, 21, 28, 28) or (21,) broadcast
- mask=1 for clean observation frames (frames 0-6: camera latents)
- mask=0 for denoising target frames (frames 7-20: action/proprio/future)
- Controls which frames are kept fixed vs. predicted by diffusion
CODE: cosmos_policy/models/policy_video2world_model.py:100 get_data_and_condition() | cosmos_policy/models/policy_text2world_model.py:246 compute_loss_with_epsilon_and_sigma()

## Slide 7
模块 5: 文本条件编码
Text Condition — Language Instruction Embedding
Cosmos Policy Inference Pipeline — RoboCasa
7 / 20
⬅ INPUT
Task instruction string: e.g. 'pick up the red block and place it on the green target'
- Raw text from the RoboCasa task specification
- Single instruction per episode (same for all frames in sequence)
⚙ FUNCTION
Encode language instruction into dense embeddings for cross-attention.
1. Tokenize instruction with T5 tokenizer.
2. Pass through frozen T5-XXL encoder (4.6B parameters).
3. Project to cross-attention dimension (1024).
4. GeneralConditioner handles dropout (classifier-free guidance training).
At inference: dropout=0, always condition on text.
5. For video-conditioned models: Text2WorldCondition extends BaseCondition
to include video conditioning context alongside text.
➡ OUTPUT
Cross-attention embedding: (B, seq_len, crossattn_dim)
- seq_len ~20-77 tokens (T5 tokenizer output)
- crossattn_dim = 1024 (matches DiT hidden dimension)
- Used in every cross-attention layer of the DiT network
CFG
Classifier-Free Guidance: During training, text is randomly dropped (10-20%).
At inference, guidance_scale controls strength of text conditioning:
predicted = uncond + scale * (cond - uncond)
CODE: cosmos_policy/conditioner.py:86 class Text2WorldCondition | :112 class GeneralConditioner

## Slide 8
模块 6: 噪声调度 (训练)
Hybrid EDM SDE — Noise Schedule
Cosmos Policy Inference Pipeline — RoboCasa
8 / 20
⬅ INPUT
Clean latent x_0: (B, 16, 21, 28, 28) [only denoise-target frames matter]
- For training: select noise level sigma from hybrid distribution
⚙ FUNCTION
Hybrid EDM noise schedule for training stability.
1. 70% probability: Sample sigma from log-normal distribution N(P_mean, P_std^2).
log(sigma) ~ N(-1.2, 1.2^2). Favors moderate noise levels.
2. 30% probability: Sample sigma uniformly from [sigma_min, sigma_max].
Ensures coverage of extreme noise levels.
3. At inference: sigma follows deterministic schedule from sigma_max to sigma_min.
4. EDM preconditioning scales the network input/output:
c_skip(sigma), c_out(sigma), c_in(sigma), c_noise(sigma) functions.
➡ OUTPUT
Noisy latent x_sigma = x_0 + sigma * epsilon:
(B, 16, 21, 28, 28) [epsilon ~ N(0, I)]
- sigma value sampled per batch from hybrid distribution
- Only mask=0 frames get noise added; mask=1 frames stay clean
EDM PRECOND
F_denoise(x, sigma) = c_skip * x + c_out * Net(c_in * x, c_noise(sigma))
c_in = 1/(sigma^2+1)^0.5 | c_out = sigma/(sigma^2+1)^0.5 | c_skip = 1 | c_noise = 0.25*log(sigma)
CODE: cosmos_policy/modules/hybrid_edm_sde.py:22 class HybridEDMSDE | :48 sample_t() | EDM formulas in MODEL_DESIGN.md section 8

## Slide 9
模块 7: DiT 网络 (扩散 Transformer)
Diffusion Transformer (DiT) — Core Denoising Network
Cosmos Policy Inference Pipeline — RoboCasa
9 / 20
⬅ INPUT
Noisy latent: (B, 16, 21, 28, 28) scaled by c_in
Timestep embedding: sigma -> c_noise -> sinusoidal embedding
Cross-attention context: (B, token_len, 1024) from text encoder
Condition mask: (B, 1, 21, 28, 28)
⚙ FUNCTION
2B-parameter Diffusion Transformer with self-attention + cross-attention.
1. Patch embedding: Flatten (16, 28, 28) spatial -> sequence of patch tokens.
2. Positional encoding: 3D RoPE (spatial + temporal position).
3. 28 DiT blocks, each containing:
- AdaLN (Adaptive Layer Norm): conditioned on timestep sigma.
- Self-Attention: attend across all frame positions (temporal + spatial).
- Cross-Attention: attend to text embedding from T5.
- Feed-Forward: GPT-2 style MLP with GELU.
4. FinalLayer: Linear projection back to (16, 28, 28) per frame.
5. 2B total parameters, bf16 mixed precision.
➡ OUTPUT
Denoised prediction F_theta: (B, 16, 21, 28, 28)
After EDM output scaling: x_hat = c_skip * x_noisy + c_out * F_theta
Only mask=0 frames carry meaningful predictions
ARCHITECTURE
Input: (B, 16, T=21, 28, 28) -> PatchEmbed -> T*784 tokens of dim 1024
-> 28x DiT blocks (SelfAttn + CrossAttn + FFN) -> FinalLayer -> (B, 16, T, 28, 28)
CODE: cosmos_policy/_src/predict2/networks/minimal_v4_dit.py:1386 class MiniTrainDIT | :1713 forward() | :389 class Attention | :583 class I2VCrossAttention | :1049 class FinalLayer

## Slide 10
模块 8: EDM 预处理
EDM Preconditioning — Input/Output Scaling
Cosmos Policy Inference Pipeline — RoboCasa
10 / 20
⬅ INPUT
Raw noisy latent x_sigma: (B, 16, 21, 28, 28)
sigma value: scalar or (B,) tensor
Network raw output F_theta: (B, 16, 21, 28, 28) from DiT
⚙ FUNCTION
EDM (Elucidating Design Space) preconditioning stabilizes diffusion training.
Mathematical formulation:
Input scaling: c_in(sigma) = 1 / sqrt(sigma^2 + 1)
Output scaling: c_out(sigma) = sigma / sqrt(sigma^2 + 1)
Skip scaling: c_skip(sigma) = 1 (unit skip connection)
Noise mapping: c_noise(sigma) = 0.25 * ln(sigma)
Network sees unit-variance input. Output combines skip (preserves signal)
with network prediction (adds correction). Key insight: as sigma->0,
c_out->0 so output approaches clean x_0 naturally.
➡ OUTPUT
Preprocessed input to DiT: c_in(sigma) * x_sigma
Final denoised estimate: c_skip(sigma) * x_sigma + c_out(sigma) * F_theta
x_0 estimate: (B, 16, 21, 28, 28) with clean observation frames untouched
CODE: cosmos_policy/models/policy_text2world_model.py:310 compute_loss_with_epsilon_and_sigma() | cosmos_policy/_src/predict2/networks/minimal_v4_dit.py:860 Timesteps embed | :884 TimestepEmbedding

## Slide 11
模块 9: 迭代采样 (去噪循环)
Iterative Denoising Loop — CosmosPolicySampler
Cosmos Policy Inference Pipeline — RoboCasa
11 / 20
⬅ INPUT
Pure noise x_T: (B, 16, 21, 28, 28) at sigma_max
- Only mask=0 frames are noise; mask=1 frames are clean obs latents
- num_steps: number of denoising steps (e.g. 35 for RoboCasa)
⚙ FUNCTION
Iterative denoising from pure noise to clean latent prediction.
1. Initialize mask=0 frames with noise at sigma_max (mask=1 frames stay clean).
2. For each step t = T, T-1, ..., 1:
a. Compute current sigma_t and next sigma_{t-1}.
b. Get x_0 prediction from denoise function (EDM + DiT).
c. Apply deterministic ODE step: x_{t-1} = x_t + (sigma_{t-1} - sigma_t) * score.
d. Special case: num_steps=1 -> directly use x_0 prediction (single step).
3. Final output: fully denoised latent sequence.
4. CosmosPolicySampler supports sample_clean=True for mask-aware sampling.
➡ OUTPUT
Denoised x_0: (B, 16, 21, 28, 28)
- mask=0 frames now contain predicted action/proprio/future latents
- mask=1 observation frames unchanged throughout sampling
SCHEDULE
Sigma schedule: geometric progression from sigma_max (~80) to sigma_min (~0.002)
ODE solver: Euler or RK4. Default: Euler with 35 steps for RoboCasa inference.
CODE: cosmos_policy/modules/cosmos_sampler.py:40 class CosmosPolicySampler | :96 _forward_impl()

## Slide 12
模块 10: VAE 解码器
WAN 2.1 VAE Decoder — Latent to Pixel
Cosmos Policy Inference Pipeline — RoboCasa
12 / 20
⬅ INPUT
Denoised latent sequence: (B, 16, 21, 28, 28)
- Only action/proprio/future frames need decoding
- In practice: decode ALL frames, then extract action channels
⚙ FUNCTION
WAN 2.1 VAE Decoder reconstructs pixel video from latents.
1. Temporal upsampling: T' -> T'*4 (inverse of 4x temporal compression).
2. Spatial upsampling: 28 -> 224 (inverse of 8x spatial compression).
3. Channel projection: 16 -> 3 (latent -> RGB).
4. Uses 3D transposed convolutions for spatiotemporal upsampling.
IMPORTANT: For action extraction, we do NOT decode to pixels.
Actions are read directly from latent frames (next module).
VAE decode is optional and mainly for debugging/visualization.
➡ OUTPUT
Decoded pixel-space video: (B, 3, T'*4, H*8, W*8)
- Per action frames: (B, 3, 32, 224, 224) — but NOT used for action extraction!
- Action values are extracted DIRECTLY from latent, not decoded pixels
- VAE decode is only used for visualization/verification
KEY INSIGHT
Actions live in LATENT space, not pixel space.
The 'fake video frame' trick means actions are stored as latent values,
not rendered as pixels. Decoding is unnecessary for robot control.
CODE: cosmos_policy/tokenizers/wan2pt1.py:341 decode() | :197 class CosmosPolicyWanVAE | :518 decode() (state encoder)

## Slide 13
模块 11: 动作提取
Action Extraction from Latent Frames
Cosmos Policy Inference Pipeline — RoboCasa
13 / 20
⬅ INPUT
Denoised latent sequence: (B, 16, 21, 28, 28)
- Action latent frames at indices 7-14 (8 frames for RoboCasa)
- Each frame: 16 * 28 * 28 = 12,544 values per frame
⚙ FUNCTION
Reverse the latent injection process to recover action values.
1. Select action latent frames by their indices in the sequence.
2. For each action frame: flatten (16, 28, 28) -> 12,544 values.
3. Take the first 28 values per frame (224 total / 8 frames = 28).
4. Reshape to (chunk_size=32, action_dim=7).
5. De-normalize: multiply by action_std, add action_mean.
6. Clamp to valid robot command range.
This is the INVERSE of replace_latent_with_action_chunk().
➡ OUTPUT
Action chunk: (B, chunk_size=32, action_dim=7)
- 32 action steps, each with 7 DoF (x,y,z,rx,ry,rz,gripper)
- Total 224 values extracted from 8 latent frames (28 values per frame)
- Values are de-normalized to robot command range
CODE: cosmos_policy/models/policy_text2world_model.py:45 replace_latent_with_action_chunk() | cosmos_policy/experiments/robot/cosmos_utils.py:851 get_action() | :61 get_latent_indices_from_model_config()

## Slide 14
模块 12: 本体感知提取
Proprioceptive State Extraction
Cosmos Policy Inference Pipeline — RoboCasa
14 / 20
⬅ INPUT
Denoised latent sequence: (B, 16, 21, 28, 28)
- Proprio latent frames at indices 15-16 (2 frames for RoboCasa)
- Each frame: 12,544 values, but only first ~5 values used
⚙ FUNCTION
Extract proprioceptive predictions from latent frames (same as action).
1. Select proprio latent frames by their indices.
2. Flatten each frame, take first ~5 values per frame.
3. Reshape to proprio_dim=9.
4. De-normalize to physical joint/gripper range.
5. The model predicts FUTURE proprio as a side effect of denoising.
Note: Proprio prediction is auxiliary — main output is the action chunk.
But it helps the model maintain temporal consistency.
➡ OUTPUT
Predicted proprio: (B, 2, proprio_dim=9) or (B, 9)
- Predicted future proprioceptive state
- Can be used for planning or state prediction validation
- 9 values: 7 joint positions + 2 gripper states
CODE: cosmos_policy/models/policy_text2world_model.py:112 replace_latent_with_proprio() | cosmos_policy/experiments/robot/cosmos_utils.py:61 get_latent_indices_from_model_config()

## Slide 15
模块 13: 机器人执行
Robot Action Execution
Cosmos Policy Inference Pipeline — RoboCasa
15 / 20
⬅ INPUT
Action chunk: (B, 32, 7) — 32 action steps, 7 DoF each
- Absolute joint positions for 7-DOF robot arm + gripper
- De-normalized to robot's joint command range
- Predicted in open-loop fashion
⚙ FUNCTION
Convert predicted action chunk to robot joint commands.
1. Action space: absolute joint positions (not delta actions).
2. De-normalize: action_raw * action_std + action_mean.
3. Clamp to joint limits.
4. Send to low-level PD controller at control frequency.
5. Gripper command: continuous value mapped to open/close.
The action chunk provides 32 steps of future control,
but only a subset is executed (see Open-Loop Control slide).
➡ OUTPUT
Joint commands sent to robot controller:
- 7-DOF joint position targets per timestep
- Executed at control frequency (e.g., 20Hz)
- Only first `execute_steps` actions are actually executed before re-planning
CODE: cosmos_policy/experiments/robot/cosmos_utils.py:851 get_action() | RoboCasa environment wrapper

## Slide 16
模块 14: 开环控制策略
Open-Loop Control Strategy
Cosmos Policy Inference Pipeline — RoboCasa
16 / 20
⬅ INPUT
Predicted action chunk: (32, 7) — full trajectory prediction
- 32 steps of future control predicted in one forward pass
- Only a subset will be executed before re-querying the model
⚙ FUNCTION
Temporal action chunking with partial execution.
1. Model predicts chunk_size=32 future action steps in ONE forward pass.
2. Only the first `execute_steps` (e.g., 4 or 8) are actually executed.
3. After execution, new observation is collected.
4. Model is re-queried with updated observation history.
5. Benefits:
- Reduces inference frequency (every 4-8 steps instead of every step).
- Provides temporal consistency within the chunk.
- Allows course-correction at each re-query.
- Trade-off: more execute_steps = faster but less reactive.
➡ OUTPUT
Executed actions: (execute_steps, 7) — typically 4-8 steps
- First `execute_steps` actions from the chunk are executed
- Then a new observation is taken and model is re-queried
- Remaining actions in the chunk are DISCARDED
TRADE-OFF
execute_steps=4: More reactive, higher inference cost, smoother corrections
execute_steps=8: Less reactive, lower inference cost, more committed to plan
RoboCasa default: typically 4-8 steps
CODE: cosmos_policy/experiments/robot/cosmos_utils.py:851 get_action() | experiment configs: execute_steps parameter

## Slide 17
模块 15: Best-of-N 规划
Best-of-N Planning — Action Selection
Cosmos Policy Inference Pipeline — RoboCasa
17 / 20
⬅ INPUT
N candidate action chunks: N x (32, 7)
- Generated by running N independent denoising passes
- Each starts from different random noise -> different action proposals
- Typically N=4 or N=8
⚙ FUNCTION
Generate multiple action candidates, rank by predicted value.
1. Run denoising N times independently (different noise seeds).
2. For each candidate: predict its expected return using value head.
3. Select the candidate with highest predicted value.
4. This is a simple but effective test-time compute scaling method.
5. More candidates = better selection but more inference time.
6. Analogous to 'sample-and-rank' in language models.
This is the PLANNING variant. For direct policy (no planning), N=1.
➡ OUTPUT
Best action chunk: (32, 7)
- Selected from N candidates based on value prediction
- The candidate with highest predicted value is chosen
- Remaining N-1 candidates are discarded
VALUE HEAD
The model also predicts a VALUE latent frame (1 scalar).
This value predicts the expected return for the given action sequence.
Used as a scoring function for Best-of-N selection.
CODE: cosmos_policy/models/policy_video2world_model.py:569 get_x0_fn_from_batch() | cosmos_policy/experiments/robot/cosmos_utils.py:851 get_action()

## Slide 18
模块 16: 价值预测
Value Function Prediction
Cosmos Policy Inference Pipeline — RoboCasa
18 / 20
⬅ INPUT
Denoised latent sequence: (B, 16, 21, 28, 28)
- Contains a value latent frame at a specific index
- Value is encoded as a scalar in one latent frame (similar to action/proprio)
⚙ FUNCTION
Predict the expected return of the proposed action trajectory.
1. A dedicated latent frame stores the value prediction.
2. Value is encoded similarly to action: scalar repeat-filled into latent frame.
3. After denoising, the value is extracted (inverse of injection).
4. Training: value_loss is masked separately from action_loss.
5. Can be disabled via mask_value_prediction_loss_for_policy_prediction.
6. The value prediction enables planning without a separate critic network.
➡ OUTPUT
Predicted value: scalar (B, 1)
- Estimated expected return for the predicted action trajectory
- Used for ranking in Best-of-N planning
- Higher value = better predicted outcome
CODE: cosmos_policy/models/policy_text2world_model.py:186-210 (value config fields) | cosmos_policy/models/policy_text2world_model.py:328 (value_function_return)

## Slide 19
模块 17: 多视角融合
Multi-View Camera Fusion
Cosmos Policy Inference Pipeline — RoboCasa
19 / 20
⬅ INPUT
3 independent camera streams, each encoded separately:
- agentview: (B, 16, 3, 28, 28)
- eye_in_hand: (B, 16, 2, 28, 28) [2 temporal frames]
- robotface: (B, 16, 2, 28, 28)
- Each captures different spatial information about the scene
⚙ FUNCTION
Fuse multiple camera views into a single latent sequence.
1. Each camera view is independently VAE-encoded.
2. All camera latents are concatenated along the temporal axis.
3. The DiT's 3D RoPE positional encoding differentiates:
- Spatial position within each view (28x28 grid).
- Temporal position across frames.
- No explicit view ID needed — position encoding is sufficient.
4. Self-attention across ALL frame tokens enables cross-view reasoning.
5. The model learns to correlate information across camera angles.
➡ OUTPUT
Unified latent sequence: (B, 16, 7+, 28, 28)
- All camera latents concatenated along temporal dimension
- Positions: frames 0-2 (cam1), frames 3-4 (cam2), frames 5-6 (cam3)
- Followed by action/proprio/future frames
- 3D RoPE positional encoding distinguishes each view's position
ROBOCASA VIEWS
agentview: overhead/front view of workspace
eye_in_hand: wrist-mounted camera on robot end-effector
robotface: side view capturing robot arm configuration
Different temporal lengths due to frame padding for 4x temporal compression.
CODE: cosmos_policy/experiments/robot/cosmos_utils.py:61 get_latent_indices_from_model_config() | cosmos_policy/tokenizers/wan2pt1.py:303 encode() (per camera)

## Slide 20
模块 18: 训练 vs 推理对比
Training vs Inference Comparison
Cosmos Policy Inference Pipeline — RoboCasa
20 / 20
TRAINING
1. Collect (obs, action, proprio, value) from expert demos
2. VAE encode all observations -> latents
3. Inject ground-truth action/proprio into latent frames
4. Create condition mask: obs=1, action/proprio=0
5. Add noise to mask=0 frames: x_sigma = x_0 + sigma * eps
6. DiT predicts noise (or x_0) from noisy input
7. Loss = MSE(predicted, target) on mask=0 frames only
8. Hybrid EDM: 70% log-normal + 30% uniform sigma sampling
INFERENCE
1. Collect current obs from robot sensors
2. VAE encode observations -> clean latents (mask=1)
3. Initialize action/proprio frames as NOISE (mask=0)
4. Iterative denoising loop (35 steps ODE solver)
5. At each step: DiT predicts x_0 from noisy input
6. ODE step updates noise toward clean prediction
7. Final denoised latents contain predicted actions
8. Extract action chunk, execute first N steps
KEY DIFFERENCES
Training: Ground-truth actions injected -> model learns to DENOISE them
Inference: Action frames start as noise -> model GENERATES them via iterative denoising
Training loss: MSE on mask=0 frames only, with optional loss masking for action/value separation
Inference: No ground truth needed, purely generative prediction from observations
CODE: cosmos_policy/models/policy_text2world_model.py:310 compute_loss_with_epsilon_and_sigma() | :702 generate_samples_from_batch() | cosmos_policy/modules/cosmos_sampler.py:96 _forward_impl()